## Slide 1: Speaker Verification Tutorial for Sony
Presented by Dr. Simon Lucey
Advanced Multimedia Processing (AMP) Labs
Carnegie Mellon University
9/5/2002-9/6/2002
(San Jose)

## Slide 2: Tutorial Schedule
AM Session, Sep. 5 (Thursday)
  10:00~11:00 Background to speech processing
  11:00~11:15 Break
  11:15~12:15 Front-end processing
PM Session, Sep. 5 (Thursday)
  1:30~3:00 Speaker models (part 1)
  3:00~3:15 Break
  3:15~4:15 Speaker models (part 2)

## Slide 3: Tutorial Schedule
AM Session, Sep. 6 (Friday)
  10:00~11:00 Speaker verification, current direction and development.
  11:00~11:15 Break
  11:15~12:15 Hardware considerations and discussion
Please ask questions?

## Slide 4: About myself
Attained my Ph.D. at Queensland University of Technology.
Thesis topic was “Audio-visual speech processing”.
Conducted research in,
  Audio-visual speaker recognition
  Audio-visual speech recognition
  Classifier combination theory
  Facial feature detection
Come from a “relatively” strong speech background.

## Slide 5
Speech Processing
Background

## Slide 6: Background – Voice Biometric
Speaker verification relies on what is often referred to as a voice biometric.
Biometric is defined as the recognition of a person based on his/her personal traits.

## Slide 7: Background - Why voice?
Is an obvious modality to use, as we as humans use acoustic speech everyday to discern between different speakers.
Is not considered threatening by users; natural to most people to use phone or microphone (non-intrusive).
Existing telephone system provide a ubiquitous, familiar network of sensors for obtaining speech.
Very mature field, as research has been carried out for the last four decades.

## Slide 8: Applications - Introduction
Speech Recognition
Language Recognition
Speaker Recognition
“what am I saying?”
“what language am I speaking?”
“who is speaking?”
input
signal
Application

## Slide 9: Applications - Speaker Recognition
Speaker recognition encapsulates two tasks,
  Speaker identification: task of determining who is talking from a set of known voices.
  Speaker verification: task of determining whether a person is who he/she claims.
Other pseudonyms for speaker verification,
  Voice authentication
  Speaker detection

## Slide 10: Applications - Speaker identification
“Which one is it Marge, Homer or Bart?”
?
?
?
N class
problem

## Slide 11: Applications - Speaker verification
“Is this Homer?”
2 class
problem
Yes?
No?

## Slide 12: Applications – Modern System
Front-end
processing

Imposter
model
Speaker model
+
-

## Slide 13: Applications - Text dependence/independence?
Dependent on the level of user cooperation.
Can either be,
  Text dependent: the recognition system has prior knowledge of the text to be spoken.
  Text independent: there is no prior knowledge by the system of the text to be spoken, such as extemporaneous.

## Slide 14: Applications - Text dependence?
Benefits
  Generally better performance, as task is constrained.
    Improvement comes from constraining speech so comparisons can be made on how speakers make specific sounds, rather than allowing for large textual variations.
  Improved security (as imposters cannot present recorded ubiquitous speech).

## Slide 15: Applications - Text dependence?
Cons
  Requires accurately transcribed speech.
  Speakers have to cooperatively speak the text.
  Must also model dynamic nature of speech.

## Slide 16: Applications - Text independence?
Benefits
  Much more flexible, can be used for extemporaneous speech.
  Does not have to model dynamic nature of speech (computational advantage).
  Superior to text dependent applications when no transcription available, or transcription is erroneous.

## Slide 17: Applications - Text independence
Cons
  Requires large amounts of phonetically balanced speech.
  Due to large textual variation, models may be very complex.

## Slide 18: Performance – FA and FR
Difficult to characterize performance of speaker verification system.
Dependent on,
  size of database;
  testing conditions;
Generally evaluated in terms of two types of error,
  False acceptance (FA) error.
  False rejection (FR) error.
Percentage of
imposters accepted
Percentage of
clients rejected

## Slide 19: Performance - FA and FR
FA and FR increase and decrease respectively, based on the threshold .
Receiver operating characteristic (ROC) curve can be used to show performance for a varying threshold.
Equal error rate (FA=FR) can also be used as an quantitative measure of performance.

## Slide 20: Performance – DET plot
Detection error tradeoff (DET) plot.
Similar to receiver operating characteristic (ROC) curves.
Becoming widely used over traditional plots as they show more detail.
If imposter and claimant scores are normal, will show as a straight line.
Allows for better comparison between techniques.

## Slide 21: DET – Example (overlap)

## Slide 22: DET – Example (overlap)

## Slide 23: DET – Example (separated)

## Slide 24: DET – Example (separated)
Improved
Performance
EER (%)

## Slide 25: Voice Biometric - History
Initially investigated by Alexander Melville Bell (father of Alexander Graham Bell) 100 years ago, studying phonetics.
Early 1940s Potter, Kopp & Green (Bell Labs) developed sound spectrogram (intensity, frequency and time).
WWII scientists suggested its use to identify enemy voices (war ended before use).

## Slide 26: Voice Biometric – History cont…
Late 50s early 60s, research intensified as NYPD was receiving many bomb threats.
Lawrence G. Kersta (Bell Labs) developed technique using spectrogram.
Used as evidence in US courts since late 60s (still regarded with some suspicion).
Techniques required human analysis of spectrogram.
From late 60s to present automated techniques for classification have been pursued.

## Slide 27: Evolution of Speaker Verification Classifiers
(Taken from Reynolds’01)

## Slide 28: Voice Biometrics – Cues
Low level cues are usually used!
(Taken from Reynolds’01)
(Higher level analysis subject of continuing research)

## Slide 29: Voice Biometric – Strengths & Weaknesses
Strengths
  high accuracy compared against other biometrics.
  in good conditions achieves excellent results.
Weaknesses
  Heavily affected by noise and other environmental conditions - depends on the speech features.
  Requires relatively large amounts of training observations
Last two points, basic focus
of research in speaker recognition
community!!!

## Slide 30: Voice Biomteric – Works best!
Ideal situation for best performance
  compare against same train/test conditions
  clean speech
  same speaking style in training and testing
  same language in training and testing

## Slide 31: Mechanics – Introduction
An understanding of the basic mechanics of speech is crucial.
Speech is a naturally varying continuous signal whose statistics change with time.

## Slide 32: Mechanics – Speech process

## Slide 33: Mechanics - Modulation

## Slide 34: Mechanics – Formants
Peaks are known as formants and represent resonances of the vocal tract.
(Taken from Reynolds’01)

## Slide 35: Spectrogram – What is?
First machines were analog, but has a clear digital interpretation.
FFT
Magnitude

## Slide 36: Spectrogram – Example

## Slide 37: Spectrogram – Example of distinction
Male “0-1-2”
Female “0-1-2”

## Slide 38: Phonetics and Phonemics - Introduction
“Meaning of what is being said”
“Mechanics of what is being said”
Phonemic
Filter
Semantic Level
Syntactic Level
Mapping function
Gives insights into why adults have difficulties learning foreign languages.

## Slide 39: Phonetics – Phonemes and Phones
Phones are the basic units of sound in a language. (syntatic, articulation)
Phoneme is a group of phones carrying the same meaning. (semantic, language)
Allophones are phones in a phoneme.
Number of phones are infinite, but tend to be clustered into 20-60 phonemes, each language.
Sound of phonemes heavily speaker dependent.

## Slide 40: Phonemics - Coarticulation
Phones are not executed uniformly, independent of context.
Phone is a target at which speech mechanism aims at, rarely achieves.
In most cases gets close enough to be intelligible.
Synthesis and recognition systems must model this coarticulation (diphones,triphones).

## Slide 41: Phonemics – What is?
Phoneme is the basic unit of speech which can change the meaning of a word.
Number of phonemes in a language may vary (eg. 11 in Rotokas (Papua New Guinea) to 141 in Xu! (Kalahari)).
“Doh”
“Bart”
Text
transcription
Phonetic
transcription
/d/ /ow/
/b/ /ah/ /r/ /t/

## Slide 42: Phonemics – Allophone example
Example of allophone can be found in words “pin” and “spin”.
Latter sounds more like a /b/ than /p/.
Allophones are heavily contextual.
No difference in meaning,
/s/ /p/ /ih/ /n/
/s/ /b/ /ih/ /n/
= “spin”

## Slide 43: Phonemics - Clustering of phonemes

## Slide 44: Syllables and Words – Putting it together
Phonemes
Syllables
Words
Coarticulation
effects
Prosidy
effects
Continuous Speech
(Local power maximum,
generally associated with
vowels)

## Slide 45: Prosidy – What is?
Prosodics, term given to aspects of speech that span groups or syllables or words.
Interested in pitch (intonation) and stress.
Stress reflects degree of emphasis with which a word or syllable is spoken.
Over phrases and sentences, prosidy gives shades of meaning beyond words themselves.
Avenue for future research.

## Slide 46
Questions?

## Slide 47
Break!

## Slide 48
Front-end
Processing

## Slide 49: Front-end processing - Introduction
Consists of three processes,
  Remove non-speech portions from the signal.
  Feature extraction.
  Channel compensation.

## Slide 50: Speech detector - Introduction
Plethora of techniques for removing silence.
Dependent on,
  Text dependent (statistical silence models)
  Text independent (energy based)
Generally speech detector discards 20-25% of the signal.
(Talk about statistical models later)

## Slide 51: Speech detector – Energy based
est(t) = short-time energy
est = long-time energy
Able to estimate SNR at time t as
Threshold
determined
empirically

## Slide 52: Speech detector – Example
(Silence removed)
(With silence)
Techniques can be improved using zero crossing rates, or statistical silence models.

## Slide 53: Feature extraction - Philosophy
Real world events can be observed from an infinite number of perspectives.
Have to restrict perspective to a finite feature space (i.e. feature extraction).
Ideal feature extraction obtains an representation of an real world event that,
  provides suitable class distinction for the task at hand (i.e. speaker verification).
  is invariant to unwanted transformations.

## Slide 54: Pattern Recognition – Classical
Classification
Feature
extraction
Distinction is not
always clear
Real World
Decision?
Keep class distinction,
remove unwanted
variation.
Generalize to true
decision boundaries, with minimal training observations.

## Slide 55: Feature extraction – Speech
Many ways to discriminate speakers based on,
  Formants;
  Stress/Energy;
  Duration;
  Pitch;
Most of these can be
found from the spectrum

## Slide 56: Features – Quantizing the Spectrum
Generally agreed that best representation comes from analysing the spectrum.
Techniques differ mainly in how they quantize the spectrum.
Two basic approaches available,
  Linear prediction analysis, and
  Filter bank analysis.
Techniques very similar.

## Slide 57: Features – Linear predictive analysis
Attempts to model speech process using an all pole filter,
Fits linear prediction coefficients (LPC) to minimize the mean square error for a window of speech.
Magnitude response of filter represents spectral envelope of speech window.

## Slide 58: Features – Linear predictive analysis
Based on the excitation-modulation model of the vocal tract,
where,
X(f) = spectrum of speech window
G(f) = glottal excitation spectrum
H(f) = vocal tract transfer function
f = frequency

## Slide 59: Features – Excitation-modulation
G(f)
H(f)
X(f)

## Slide 60: Features – Robust representation
LPC form is not robust to distortions of mismatches between train/test conditions.
Employ a cepstral representation,
“iterative relation”
Known as linear predictive cepstral coefficients (LPCCs).

## Slide 61: Cepstrum – Introduction
The cepstrum is the inverse Fourier (or similar) transform of the logarithm of its power spectrum.
First coined by J. R. Turkey in 1963.
As the name suggests the cepstrum operation turns the spectrum “inside out”.
spectrum
cepstrum

## Slide 62: Cepstral features – Definition
Can be defined as,
where,
C(q) = cepstrum representation
T{}= transform (usually DCT)
q = quefrency

## Slide 63: Cepstral features - Benefits
Channel effects become additive (more on this).
Features are uncorrelated due to transform T{} (usually DCT).
Robust to distortions and channel effects.
Because of these properties,
cepstral representations almost
always used!

## Slide 64: Features – Filterbank analysis
Based on how human ear resolves frequencies non-linearly.
More direct than LPCCs.
Accesses spectrum directly.
Bins the magnitude mi of each non-linearly placed filter bank.
Uses triangular mel-scaled filterbanks.

## Slide 65: Features – Mel-scale
Mel-scale defined as,

## Slide 66: Features – MFCCs
Also uses cepstral representation,
Referred to as Mel-frequency cepstral coefficients (MFCCs).
where,
N = number of filter banks
mi = ith filter bank energy value

## Slide 67: Comparison – LPCCs vs MFCCs
Both techniques obtain similar results (differ only quantization of magnitude spectrum).
At the moment MFCCs have been shown empirically to perform best for the task of speaker verification.

## Slide 68: Channel Compensation - Introduction
Large problem in pattern recognition community.
Known more generically as “train/test” mismatch.
Occurs when conditions for training differ from testing (real world problem).
Need intelligent approaches to generalize knowledge to make confident decisions in these unknown conditions.

## Slide 69: Channel Compensation – Difficulties
Human produced sound artifacts
  lip smacks, heavy breathing, clicks, pops.
Distortion in transmission system,
  cross talk, intermodulation distortion, tonal interference.
Environmental conditions
  stationary noise (fans, machinery, etc.)
  non-stationary noise (door slams, road noise)
  speech interference (TV, radio, other talkers)
  hostile environments (speech in stress)

## Slide 70: Feature Compensation – Introduction
If one can provide invariance to these type of mismatches, at the feature level, the entire system will reap the benefits.
Number of techniques can be employed,
  Cepstral weighting.
  Cepstral mean subtraction.
  Delta and acceleration coefficients.
  Other robust techniques.

## Slide 71: Compensation – Cepstral weighting
Attempts to compensate for the sensitivity of the low-order cepstral coefficients to overall spectral slope.
Also addresses sensitivity to of high-order cepstral coefficients to noise.
Known as liftering.

## Slide 72: Compensation – Liftering
Weighting
Cepstral coefficient index

## Slide 73: Compensation – Cepstral subtraction
Channel effects in cepstrum are additive,
Assuming the mean of clean speech is zero, one can compensate for channel effects,
“Distortion”
“Clean spectrum”
Very dependent on the length of the speech segment, and stationarity.

## Slide 74: Compensation – CMS
Often referred to as cepstral mean subtraction (CMS).
Technique works very well in noisy conditions.
Affects performance in clean conditions.

## Slide 75: Compensation – Delta features
Delta features operate under a similar philosophy to CMS.
Interested in the relative difference between adjacent features.
Delta and static observation vectors usually concatenated into a single observation vector.
Has been shown empirically to improve performance.

## Slide 76: Compensation – Other approaches
Relative spectral (RASTA) technique has been investigated as another compensation technique.
Works on the basis that the rate of change of nonlinguistic components in speech often lies outside the typical rate of change of the vocal-tract shape.
Essentially tries to filter out these nonlinguistic components.
Has shown some improvement.

## Slide 77
Questions?

## Slide 78
Break!

## Slide 79
Speaker
Modeling

## Slide 80: Speaker Modeling - Introduction
Speaker models spkrcreated to approximate process of speech production for a speaker.
Only concerned with discriminative process of spkr, not total process.
Good speaker model must be,
  Based on a theoretical underpinning, allowing for extensions and improvements.
  Generalizable to new observations.
  Parsimonious in size and computation.

## Slide 81: Speaker Modeling – Classifier Theory
Interested in discrimination, not synthesis or coding.
Classifier theory gives a framework, for generating such models.
Optimal classifier is Bayes classifier,
Ratio of likelihoods between
speaker and general population
Threshold selected based
on required
FA and FR
Classifier can try and obtain likelihoods or decision boundary explicitly.

## Slide 82: Classifiers – Practical limitations
Can never obtain true likelihood functions due to,
  finite number of training observations;
  unknown parametric form of process (i.e. hidden processes).
Given a finite and noisy data set different classifiers will realise different decision boundaries.

## Slide 83: Classifiers – Optimal classifier?
Performance of classifier is heavily problem dependent.
There is no one classifier that can solve all classifier problems.
Neural network community
guilty of spreading this myth!!!

## Slide 84: Classifiers – Approaches
Can only ever approach Bayesian classifier.
Many different types of classifiers available.
All can be derived in terms of trying to mimic the behavior of Bayes classifier using some assumptions.

## Slide 85: Classifiers – Difference unclear?
Classification
Feature
extraction
Distinction is not
always clear
Real World
Decision?
Keep class distinction,
remove unwanted
variation.
Generalize to true
decision boundaries, with minimal training observations.

## Slide 86: Classifiers – Assumptions for speech
To start with deal only with text-independent scenario (text dependence later).
Assume a given utterance takes the form,
where ot is a D dimensional observation vector (typically cepstral coefficient).
Assume independence such that,

## Slide 87: Classifier – Assumptions for speech
Assumes no hidden processes for speech.
Approximation is sufficient for text-independent case.
Text dependent case more difficult, have to assume a hidden process.
Text-independent case translates up to text-dependent case.
Text-independent classifiers are used as building blocks for modeling the text-dependent hidden process.

## Slide 88: Classifier – Speaker distinction?
Different problems require different approaches to classification, e.g.
Decision
from
single
observation
Face Verification
Decision
from
multiple
observations
Speaker Verification

## Slide 89: Classifier – Speaker distinction

## Slide 90: Classifier – Speaker distinction
Emphasis placed on aggregate separation of distributions, rather than individual observations.

## Slide 91: Classifiers - Types
Three broad categories of classifiers
  Discriminative (decision boundary)
  Non-parametric (observations)
  Parametric (distribution)
Special emphasis on parametric classifiers
for speaker verification

## Slide 92: Classifiers – Non-parametric
Makes no assumption about the speaker model distribution.
Relies totally on training observations.
Operates under philosophy,
where,
k – number of observations in window
n –number of total observations
V – volume of window
Estimate becomes more accurate as n -> infinity and V -> 0 !!!

## Slide 93: Non-parametric – Nearest Neighbor
In practice only have a finite amount of samples.
Nearest neighbor strategy natural extension.
Attempts to find nearest labeled observation to the test observation using some distance measure D().
Correlation filters can be interpreted as a nearest neighbor classifier.

## Slide 94: Nearest Neighbor - Example
Nearest neighbor

## Slide 95: Classifiers – Non-parametric
Technique works well when there is limited knowledge describing classes.
Tasks like face verification use non-parametric classifiers with good results.
Tasks where there are large amounts of observations, less attractive.
Due to storage limitations and computational tractability.
Adaptation to new conditions is messy.

## Slide 96: Classifiers - Discriminant
Discriminant classifiers commonly used in many tasks.
Typical discriminative classifiers are,
  Artificial Neural Networks (ANNs)
  Support Vector Machines (SVMs)
Attempt to find decision boundary not likelihood function.
Training involves all classes.

## Slide 97: Discriminant classifiers - Example
Finds decision
boundary
Does not
explicitly
find likelihood
functions

## Slide 98: Discriminant classifiers - Problems
Results up until now have been poor in literature for speaker verification,
Attributed to a number of factors,
  Adaptation to new conditions not mathematically clear (channel conditions) as likelihood function is not found directly.
  Discriminant classifiers tend to separate individual observations, not distributions.
  Interclass dependence makes training difficult and computationally intensive.

## Slide 99: Classifiers - Discriminant
Jury is still out on the use of discriminant classifiers in speaker verification.
Avenue for future research.
Discriminant classifiers tend to be well suited to problems,
  where the number of classes is well defined.
  minimal mismatch between training and testing conditions.
Have found their niche in computer vision problems (i.e. object detection and recognition).

## Slide 100: Parametric classifier - Introduction
Parametric classifiers are the classifier of choice in speaker verification.
Have benefits, over other classifiers, for tasks where,
  there are a large number of observations;
  adaptation to different testing conditions is required;
  variable number of classes exist (i.e. number of clients);
  a firm mathematical formalism is required, for extension and adaptation.

## Slide 101: Parametric classifier – What?
Parametric classifiers try to find parametric representation of likelihood function p(o|
Useful for problems with large amounts of observations.
Represent an infinite number of observations, using a finite parametric representation.

## Slide 102: Parametric classifiers – Example
Decision
boundary
results indirectly.
Explicitly
find likelihood
functions

## Slide 103: Parametric classifiers – Problems
Faced with two problems,
Estimation (finding model 
Evaluation (finding how well the utterance O fits model )
Estimation usually most difficult!!!

## Slide 104: Parametric classifiers - Problems
Rarely have access to parametric representation .
Only have access to training observations.
Have to estimate
from observations
and prior assumptions

## Slide 105: Parametric classifiers – Estimation
Training observations give no information on parametric form (i.e. Gaussian, Laplacian, Cauchy).
Example, for a Gaussian distribution p(o), parametric form  = [,] where,
= mean
 = covariance
Can make a piece wise approximation
Using Gaussian mixture models (GMM)!!!

## Slide 106: PDF – What is an pdf?
A probability density function (pdf) (i.e. the explicit distribution) describes the probability that an observation will exist within a certain range.
Formally,

## Slide 107: PDF – Alternative Interpretation
The size of a sample of a probability density function indicates how likely a particular sample is to be found in the neighbourhood of a value.
A PDF must satisfy,

## Slide 108: PDF – Likelihoods and pdfs
In literature terms likelihood function and probability density function sometimes used incorrectly.
PDF can always be referred to as a likelihood function.
However, likelihood function cannot always be referred to as an PDF.

## Slide 109: PDF – Likelihoods and pdfs
In terms of class decisions they are identical,
Likelihood functions do not have to integrate to unity!
When evaluating either function for an observation o*,

## Slide 110: PDF - Likelihoods
Unless otherwise specified, always refer to likelihood functions as they are more general than pdfs for classification purposes.
Gaussian and Gaussian mixture models are all pdfs (i.e. integrate to unity).
Other complicated techniques cannot assume pdfs (e.g. HMMs, ANNs).

## Slide 111: Gaussian distribution – Introduction
Many distributions Gaussian “bell” shaped.
Described totally by 2nd order moments,
That is all information contained in,
    Mean , and
    Covariance 



## Slide 112: Gaussian distribution - Usefulness
Gaussian distributions are useful when trying to gather statistics about an training observation set.
Other distributions prone to errors, as they rely on higher order moments (i.e. skew, kurtosis).
Dependent on outliers, that maybe erroneous.
Gaussian distributions generalize well, using small amounts of observations.

## Slide 113: Gaussian distribution – Why?
Gaussian distributions are very common in natural phenomena.
Due to central limit theorem,
“the aggregate effect of a large number of small, independent
random disturbances will lead to a Gaussian distribution.”
Due to this effect many distributions can be approximated by a Gaussian, or mixture of Gaussians (GMM).

## Slide 114: GMM – Introduction
Obviously not
Gaussian!!

## Slide 115: GMM – Fitting mixtures
Piece-wise fit
using a mixture of
Gaussians

## Slide 116: GMM – Aggregate effect
Aggregate result
fits distribution
well!!!

## Slide 117: GMM – Multidimensional analysis
Multi-dimensional analysis of features is important for improving source classification.
More speaker dependent information can be extracted by modelling features using a multi-dimensional space.
Speech features are multidimensional
  ie. Each “sample” comprises of more than one number.
  Multidimensional analysis is important

## Slide 118: GMM – Multidimensional example
Multidimensional Gaussian distribution,

## Slide 119: GMM – Multidimensional example
Multidimensional GMM,

## Slide 120: GMM – 2-D Example
By considering one dimension only, for each of the two feature element types, reveals a reasonable likelihood score with each 1-dimensional pdf model.

## Slide 121: GMM – 2-D example cont…

## Slide 122: GMM – 2-D example cont…
In a 2-D space, this point has a relatively low likelihood. This would not be apparent using a single variable pdf.

## Slide 123: GMM – 2-D example cont..

## Slide 124: GMM – Definition
The pdf is estimated by the summation of a set of weighted Gaussian distributions,
where,
M = no. of mixtures
i = mean of ith mixture component
i = covariance of ith mixture component
ci = ith mixture component weighting
N(,) = normal distribution
weightings must
satisfy,

## Slide 125: GMM – Components of an GMM
The Estimation Phase
The Evaluation Phase

## Slide 126: GMM – Estimation (dilemma)
Have to find
balance between
opposing forces
Classifier
complexity.
No. of
training
observations

## Slide 127: GMM – Complexity
As complexity increases (i.e. no. of free parameters) the no. of training observations required increases at an approximately exponential rate.
No. of free parameters
Required training observations

## Slide 128: GMM – A balance?
These two opposing forces can reach some sort of equilibrium based on,
  no. of training observations; and
  nature of the problem domain (i.e. how well clustered the training observations are).
  any assumptions of independence.

## Slide 129: GMM – Tools for balancing
Balance found through a number of avenues,
  Tuning no. of mixtures.
  Make assumptions about the covariance matrices of each mixture.
  Assuming independence between different subsets of the feature space (i.e. high and low fequency bands).
  A priori assumptions about nature of model (e.g. variance floors)

## Slide 130: Balance – No. of mixtures
Selecting the no. of mixture components
Model over-fitting
  Too many mixtures used for the observations the Gaussians were meant to describe.
Model under-fitting
  Too few mixtures used to approximate the pdf for more complex observation distributions.
It is imperative to select a suitable number of mixtures!!

## Slide 131: Balance – Overfitting example
Starts to
overfit

## Slide 132: Balance – Covariance representations
GMMs can take on a number of forms based on the form their covariance matrices take on.
Two most common are,
  Full covariance, and
  Diagonal covariance.

## Slide 133: Covariance representations – example
Full covariance
Diagonal covariance
“zeros in off diagonals”
no. of free parameters (i.e. O())

## Slide 134: Balance – Covariance representations
In speech applications it has been shown empirically that diagonal covariance matrices achieve better performance.
Computationally less expensive as the inverse of a diagonal matrix is the inverse of the elements along the diagonal.

## Slide 135: Balance – Assumptions of independence
Assuming independence between subsets of feature space, can aid in effective model estimation.
Such that,
where the feature space has been segmented such that o = [o{1}, o{2}].
Approximation is valid in the presence of narrow band noise.
Aim that O({1}O({2}O(

## Slide 136: Balance – A priori assumptions
Often no of training observations is still too small to create a suitably complex model.
Can restrict the values that parameters in  can take on.
Called Maximum a posteriori (MAP) estimation.
Simple example is variance flooring.

## Slide 137: Assumptions – Variance flooring
When evaluating an Gaussian need to find the inverse of the covariance matrix.
If there are not enough linearly separable observations the covariance matrix will be singular (i.e. determinant of zero).
Can circumvent this problem by forcing main diagonals of  to be above a variance floor.
“More on
MAP later”
Has been shown empirically to work well.

## Slide 138: GMM – Parameter Estimation
How do we find values of ?
Two techniques,
  Maximum likelihood (ML) estimation.
  Maximum a posteriori (MAP) estimation.
Most of the time these techniques are identical if a non-informative prior is assumed.
That is,  is allowed to take on any value as there is no evidence to the contrary.

## Slide 139: GMM – ML Estimation
Given N classes (i.e. speakers), with N observations sets S{i}, one assumes,
“drawn from”
One can assume independence between classes so abandon class notation.
Problem is to find parametric form from just the observation set S.

## Slide 140: GMM – ML Estimation
Only have a finite number T of observations,
ML estimate  is the one that maximizes,
Which is equivalent to, due to the assumption of independence,

## Slide 141: Estimation – EM algorithm
An GMM is determined by an iterative process termed the expectation maximization (EM) algorithm.
It uses an old estimate of the model parameters and provides a better guess for the next cycle.
This “improve on the previous guess” process repeats until the algorithm finds a local optimum (ie. it converges).

## Slide 142: GMM – Estimation convergence

## Slide 143: GMM - Initialization
As the EM algorithm is iterative, so is dependent on the initial guess.
Number of approaches,
  random seeding;
  k-means clustering;
  bootstrapping.
Results are not too dependent on initialization, but k-means clustering tends to be most robust.

## Slide 144: GMM – Evaluation
Speaker verification is a two class problem.
Distinguish between client and background.

## Slide 145: Speaker verification task
Front-end
processing

Imposter
model
Speaker model
+
-

## Slide 146: GMM – Background models
Background speaker modelling is the process of using non-target speaker speech to develop a series of comparative models to normalise the target speaker scores by.
Have to model background “impostors”.
Two approaches,
  World background model;
  Set of background models.

## Slide 147: Background – Why use?
Improves performance in comparison to direct likelihood thresholding.
It is more robust to additive noise and channel effects.
It is a form of speaker normalisation.

## Slide 148: Background – Why use?
oa
ob
Without imposter model
oa and ob will receive
the same likelihood score

## Slide 149: Background – Set of background models
Speech from
subpopulation 1
Speech from
subpopulation 2
bck
EM
Training
EM
Training
Combine
Models
sub1
sub2

## Slide 150: Background – World background model
EM
Training
Speech from
subpopulation 1
Speech from
subpopulation 2
bck

## Slide 151: Background – Subpopulations
Subpopulations can be considered as complicated as individual speakers (cohorts), or as simple as sex (male/female).
Empirically it has been shown that UBMs tend to perform better and are simpler, although some separation is useful.
One has to be careful that observations are pooled evenly across all subpopulations.
Cohorts have the advantage of creating a more discriminant background model.

## Slide 152: Background - Considerations
Usually should compare against same gender speakers.
Same language as the background speakers.
Similar noise and environmental conditions.
Number of background speakers.

## Slide 153
Questions?

## Slide 154
Break!

## Slide 155
Speaker
Modeling II

## Slide 156: Speaker modeling – Text dependence
Up until now talking about the text independent task.
For text-dependent case observations have been produced by a hidden process .
Can no longer assume independence between adjacent observations in an utterance.

## Slide 157: Dependence - Approaches
Number of approaches have been employed to model temporal dependence of speech,
  templates,
  dynamic time warping
  hidden markov models (HMMs)
“Concentrate on HMMs”

## Slide 158: Approaches – Templates
Compare
using distance metric
Known speaker saying “0-1-2”
Unknown speaker saying “0-1-2”

## Slide 159: Approaches - Templates
Utterances are usually different lengths.
Classical approach is to linearly stretch or compress utterance.
Flawed approach,
  requires accurate end-point identification.
  does not allow for time variation within a word.

## Slide 160: Approaches – Dynamic time warping
Dynamic time warping tries to non-linearly match a template to minimize a cost function.
Requires the computation of an warping function.
Can be viewed as an dynamic programming problem.
Can be solved using Viterbi decoding (discuss soon).

## Slide 161: Approaches – Dynamic time warping
Warping function
to align template

## Slide 162: Templates - Problems
Analogous to the nearest-neighbor approach used for the text-independent case.
Does not effectively model fluctuations.
Becomes problematic with large amounts of utterances,
  storage; and
  computation.
Require some sort of statistical approach.

## Slide 163: HMMs - Introduction
Can consider temporal speech a hidden Markov process.
Referred to as “hidden” as the internal states of the process cannot be observed.
Have to be determined from training observations and a priori knowledge.
Useful for modeling speech, as each state can be assumed to “roughly” correspond to a phonemic event.

## Slide 164: Markov model – What is?
Markov model is a finite state machine.
Markov process may be described as being in N discrete states.
Discrete states in a Markov model are represented by nodes and, the transition probabilities aij by links.

## Slide 165: Markov model – Example

## Slide 166: HMM – Coin example
A series of coin tossing experiments is performed. The number of coins is unknown; only the results of each coin toss are revealed. Thus a typical observation sequence is,
Problem: Build an HMM to explain the observation sequence!!

## Slide 167: HMM – 1 Coin example
1
2
HEADS
TAILS
P(H)
P(H)
1-P(H)
1-P(H)
X=[H,H,H,T,T,H,T,T,T]
q=[1,1,1,2,2,1,2,2,2]
Pretty
simple!!

## Slide 168: HMM – 2 Coin example
1
2
COIN 1
COIN 2
a11
1-a11
X=[H,H,H,T,T,H,T,T,T]
q=[1,2,1,2,1,1,2,1,2]
What if
one coin
is biased?
Observations
and states no
longer correspond
a22
1-a22
P(H) = P1
P(H) = P2
P(T) = 1-P2
COIN 2
P(T) = 1-P1
COIN 1
Task to
find Pi
and aij.
Not seen!

## Slide 169: Markov models – Order n models
Given a state sequence,
Normally a probabilistic description of q requires the current state at time t and all predecessor states.
However, an order 1 Markov chain probabilistic dependence is truncated to just the previous state.

## Slide 170: Markov models – Transition probabilities
Situation is further simplified as,
probabilities are invariant to time, referred to as “transition probabilities”.
Obeys following properties,

## Slide 171: Markov model - Evaluation
Given a state sequence,
and Markov model (A,, where  is a vector containing initial state probabilities at t=1.
One can evaluate the a posteriori probability of the process as,

## Slide 172: HMM - Evaluation
Typically do not have access to the state sequence, only the observation sequence.
The a posteriori probability that the observation sequence O was created by  is,
“typically evaluated as a likelihood”

## Slide 173: HMM – Evaluation
How do we evaluate?
where,
bj(o) = emission likelihood
Emission likelihood typically GMM, but maybe ANN, SVM or even another HMM!

## Slide 174: HMM – Viterbi approximation
In practice the evaluation of all possible paths too computationally intensive,
Employ Viterbi approximation,
Finds single best path q* that best describes observation sequence.

## Slide 175: HMM – Viterbi decoding
optimal state path q*
Dynamic programming
problem!!
“HMM Trellis”

## Slide 176: HMM – Viterbi decoding
To solve globally still need to evaluate every possible path.
Can solve efficiently using dynamic programming.
Most common optimality criterion is to choose states qt that are individually most likely at each time t.
Only a locally optimal solution.
Has been shown empirically to perform well.

## Slide 177: HMM – Estimation?
HMM model  defined as (,A,B),
where,
= vector of N initial state probabilities
A = NxN matrix of transition probabilities
B = vector of N emission likelihood functions
Problem is to find  from a set of training utterances S.
R is no. of training utterances

## Slide 178: HMM – Types of HMM
Different types of HMMs possible; dependent on,
  form of transition probabilities; and
  form of emission like-lihoods

## Slide 179: Types – Ergodic vs. Left to right
“Left to right”
“Ergodic”
Left to right used!

## Slide 180: Types – Ergodic vs. Left to right
Left to right topology normally employed.
Enforces causality of speech.
Also gives less free parameters (i.e. less training observations required).
Ergodic topology sometimes used to model non-causal signals (e.g. silence).

## Slide 181: Types – Discrete vs. Continuous
The emission likelihoods can be discrete or continuous.

## Slide 182: Types – Discrete vs. Continuous
Discrete emission likelihoods usually created via a vector quantization process.
Continuous likelihoods created using GMMs.
Continuous likelihoods are nearly “always” used now.

## Slide 183: HMM – Estimation?
Want to maximize ML criterion,
Two techniques used for estimation,
  Viterbi; and
  Baum Welch algorithm, (Forward Backward algorithm)

## Slide 184: HMM – Estimation considerations
Need to select,
  number of states; and
  number of mixtures (for emission likelihood function).
Dependent on,
  amount of training observations; and
  type of event being modeled.
Usually related to the number of phonemic events in the utterance.

## Slide 185: Viterbi - Estimation
Enforces a hard boundary solution.
Initially segments training utterance into N (no. of states) even segments,
q{1}= 1,1,1,1,1,1,2,2,2,2,2,2,3,3,3,3,3,3
State 1
State 2
State 3

## Slide 186: Viterbi – Estimation
q{T}=1,1,1,1,1,1,2,2,2,2,2,2,2,2,2,3,3,3
State 1
State 2
State 3
From state labels q{t}calculate new HMM model {t}.
Iterate until no change in p(S|{t+1}),

## Slide 187: Baum-Welch - Estimation
Does not define explicit boundaries in utterance.
Defines soft boundaries (i.e. observations can come from all states).
State 1
State 2
State 3

## Slide 188: Baum-Welch - Estimation
Similarly from soft labels calculate new HMM model {t}.
Iterate until no change in p(S|{t+1}),
State 1
State 2
State 3
Baum-Welch estimation tends to get best results!!!

## Slide 189: HMM – Background models
Similar concerns as for the text independent scenario involving GMMs.
Background models required to improve overall performance.

## Slide 190: Composite HMMs - Evaluation
Can be used to evaluate multiple word units, as one giant “composite” HMM.
“two”
“silence”
“silence”
“one”
“silence”
“word unit”
“Word unit
entry point”
“Word unit
exit point”
No cost associated with entry and exit points

## Slide 191: Composite HMMs - Estimation
Similarly can perform estimation on “composite” HMMs.
Extremely useful when one does not have transcribed speech for estimation.
Can still train models if one simply knows the label content of the speech.
This is how continuous speech recognizers are trained.

## Slide 192
Questions?

## Slide 193
End of
Day 1 !